## Slide 1: Management of Streaming Data
John Porter

## Slide 2
Streaming data from a network of ground-water wells

## Slide 3: What is Streaming Data?
Streaming data refers to data:
  That is typically collected using automated sensors
  Collected at a frequency more than one observation per day
    Often at a frequency of once per hour or higher (sometimes much higher)
  Collected 24-hours per day, 365 days per year
Often streaming data is collected by wirelessly networked sensors, but that is not always the case.

## Slide 4: Why Streaming Data?
Some phenomena occur at high frequencies and generate large volumes of data in a relatively short time period
  Visits of birds to nests to feed chicks
  Changes in wind gusts at a flux tower
Some data may be used to dictate actions that need to occur in short time periods
  Detection of rain event triggers collection of chemical samples
  Notification of problems with sensors

## Slide 5: Steaming Data
Frequency of Measurement
Spatial
Extent
Annual
100 km
Monthly
Weekly
Daily
Hourly
Min. Sec.
10 km
1 km
100 m
10 m
1 m
10 cm
=Paper in 2003 Ecology
Wireless
Sensor Networks
Porter et al. 2005, Bioscience

## Slide 6: Challenges for Streaming Data
Data volume – high frequency of data collection means lots of data
  Challenges for transport (hence wireless networks)
  Challenges for storage
  Challenges for processing
Providing adequate quality control and assurance
  Detection of corrupted data
  Detection of sensor failures
  Detection of sensor drift

## Slide 7: Challenges
Lots of the tools and techniques used for less voluminous data just don’t work well for really large datasets
  “Browsing” data in a spreadsheet is no longer productive (e.g., scrolling down to line 31,471,200 in a spreadsheet is an all-day affair
  Some software just “breaks” when datasets get to be too large
    Memory overflows
    Performance degradation
Notes: FYI 31,471,200 is the number of seconds in a year.

## Slide 8
Slide from Susan Stafford

## Slide 9: Storage - High Data Volumes
Some sensors or sensor networks are capable of generating many terabytes of information each year
  E.g., the DOE ARM program generates 0.5 TB per day!
Databases can run into severe problems dealing with such huge amounts of data
  Often data needs to be stored on tape robots
Frequently data is kept as text or in open source standard files (e.g., netCDF, openDAP)
  Data is Segmented based on
    Time
    Location
    Sensor
  File naming conventions are used to make it easy to extract the right “chunk” of data

## Slide 10: Common Streaming Data Errors
Corrupted Date or Time
  Can be corrected – IF it is noticed before the clock is reset
Sensor Failures
  Relatively easy to detect
  May be impossible to fix
  But sometimes estimated data can be substituted
Sensor Drift
  Difficult to detect – especially over short time periods
  Limited correction is possible, if the drift is systematic

## Slide 11: Browsing your data to look for errors is not an option!
The data is simply too voluminous for you to scan the data by eye!
Need: Statistical Summaries, Graphics or Queries to identify problems

## Slide 13: Archiving and Publishing Data
Porter, Hanson and Lin, TREE 2012
Notes: Most field ecologists are focused on “level 0” data – but the greatest opportunities for shared data are for higher-level data products. The Level 1 and Level 2 data are what are likely to be most in demand.

## Slide 14: Some Best Practices
ALWAYS preserve copies of your “Level 0” raw data
  Cautionary tale: Ozone data
    “Hole” over Antarctica was initially listed as missing data due to unexpectedly low values in processed data
Alterations to data should be completely documented
  Easiest way to do this is to use programs for data manipulation
  Very difficult to do if you edit files or spreadsheets – requires very detailed metadata
It is not unusual for data streams to be completely reprocessed using improved QA/QC tools or algorithms

## Slide 15: Some simple guidelines for effective data management*
Use a scripted program for analysis.
Store data in nonproprietary software formats (e.g., comma delimited text file, .csv); proprietary software (e.g., Excel, Access) can become unavailable, whereas text files can always be read.
Store data in nonproprietary hardware formats.
Always store an uncorrected data file with all its bumps and warts. Do not make any corrections to this file; make corrections within a scripted language.
Use descriptive names for your data files.
Include a “header” line that describes the variables as the first line in the table.
Use plain ASCII text for your file names, variable names, and data values.
When you add data to a database, try not to add columns; rather, design your tables so that you add only rows.
All cells within each column should contain only one type of information (i.e., either text, numerical, etc.).
Record a single piece of data (unique measurement) only once; separate information collected at different scales into different tables. In other words, create a relational database.
Record full information about taxonomic names.
Record full dates, using standardized formats.
Always maintain effective metadata.
* Borer et al. 2009. Bulletin of the Ecological Society of
America 90(2):205-214.

## Slide 16: Some simple guidelines for effective data management*
Use a scripted program for analysis.
Store data in nonproprietary software formats (e.g., comma delimited text file, .csv); proprietary software (e.g., Excel, Access) can become unavailable, whereas text files can always be read.
Store data in nonproprietary hardware formats.
Always store an uncorrected data file with all its bumps and warts. Do not make any corrections to this file; make corrections within a scripted language.
Use descriptive names for your data files.
Include a “header” line that describes the variables as the first line in the table.
Use plain ASCII text for your file names, variable names, and data values.
When you add data to a database, try not to add columns; rather, design your tables so that you add only rows.
All cells within each column should contain only one type of information (i.e., either text, numerical, etc.).
Record a single piece of data (unique measurement) only once; separate information collected at different scales into different tables. In other words, create a relational database.
Record full information about taxonomic names.
Record full dates, using standardized formats.
Always maintain effective metadata.
Maintain information needed for the “provenance” of the data. Allows you to backtrack, reprocess etc.

## Slide 17: Some simple guidelines for effective data management*
Use a scripted program for analysis.
Store data in nonproprietary software formats (e.g., comma delimited text file, .csv); proprietary software (e.g., Excel, Access) can become unavailable, whereas text files can always be read.
Store data in nonproprietary hardware formats.
Always store an uncorrected data file with all its bumps and warts. Do not make any corrections to this file; make corrections within a scripted language.
Use descriptive names for your data files.
Include a “header” line that describes the variables as the first line in the table.
Use plain ASCII text for your file names, variable names, and data values.
When you add data to a database, try not to add columns; rather, design your tables so that you add only rows.
All cells within each column should contain only one type of information (i.e., either text, numerical, etc.).
Record a single piece of data (unique measurement) only once; separate information collected at different scales into different tables. In other words, create a relational database.
Record full information about taxonomic names.
Record full dates, using standardized formats.
Always maintain effective metadata.
* Borer et al. 2009. Bulletin of the Ecological Society of
America 90(2):205-214.
Store data in forms that will be slow to become obsolete

## Slide 18: Some simple guidelines for effective data management*
Use a scripted program for analysis.
Store data in nonproprietary software formats (e.g., comma delimited text file, .csv); proprietary software (e.g., Excel, Access) can become unavailable, whereas text files can always be read.
Store data in nonproprietary hardware formats.
Always store an uncorrected data file with all its bumps and warts. Do not make any corrections to this file; make corrections within a scripted language.
Use descriptive names for your data files.
Include a “header” line that describes the variables as the first line in the table.
Use plain ASCII text for your file names, variable names, and data values.
When you add data to a database, try not to add columns; rather, design your tables so that you add only rows.
All cells within each column should contain only one type of information (i.e., either text, numerical, etc.).
Record a single piece of data (unique measurement) only once; separate information collected at different scales into different tables. In other words, create a relational database.
Record full information about taxonomic names.
Record full dates, using standardized formats.
Always maintain effective metadata.
* Borer et al. 2009. Bulletin of the Ecological Society of
America 90(2):205-214.
Make the data easy to use for people and a wide variety of software

## Slide 19: Processing of Streaming Data
New Data
Previous Data
Merge Data
Transformations & Range Checks
“Problem” Observations
Eliminate Duplicates
Integrated
Data
Analysis
Visualization

## Slide 20: Workflows for Processing Streaming Data
The previous diagram describes a “workflow “ for processing streaming data
The workflow needs to be able to be run at any time of the day or night – whenever new data is available
The workflow needs to be able to be completed before new data is available
What tools are available for use?

## Slide 21: Tools for Streaming Data
Typically spreadsheets are a poor choice for processing streaming data
  They are oriented around human operation, not automated operation
  They work poorly when you are dealing with millions, rather than thousands, of observations
Statistical Packages (R, SAS, SPSS etc.)
Database Management Systems (DBMS)
Proprietary software from vendors (e.g., Loggernet, LabView etc.)
Scientific Workflow Systems (e.g., Kepler)

## Slide 22: Quality Control and Assurance
QA/QC is critical for streaming data
  If you have 2 million data points and they are 99.9% error free that still means that you have 2000 bad points!
  Especially serious for detection of extreme events (maximum and minimum are often seriously affected)

## Slide 23: Standard QA/QC Checks
Does the variable type match expectations?
  Expect a number, but get a letter
Ranges – are maximum and minimum values within possible ( or expected) ranges?
  Can be conditional, such as season-specific ranges
Spikes – impossibly abrupt changes

## Slide 24: QA/QC
Quality Assurance and Quality Control for streaming data often involves “tagging” data with “flags” that indicate something about the quality of the data
“Flagging” systems tend to be dataset-specific
Var1 | Var1_Flag | Meaning
10.3 |  | OK value
15.9 | R | Value exceeds expected range
11.3 | E | Estimated value used to fill a gap in the data
 | M | Value is missing or null
15.0 | Q | Questionable value, sensor may be experiencing drift

## Slide 25: Advanced QA/QC
When streaming data includes lots of different, but correlated variables
  Predict values for a variable based on other variables
  Look for times when the predicted values are unusually poor – that is observed and predicted values don’t agree

## Slide 26: Streaming data: A Real-world Example
Here is an outline of how meterological data has processed at the VCR/LTER since 1994
  Campbell Scientific “Loggernet” collects raw data to a comma-separated-value (CSV file) on a small PC on the Eastern Shore via a wireless network
  Every 3 hours , MSDOS BATCH file copies the CSV file to a server back at the Univ. of Virginia
  Shortly thereafter, a UNIX shell-script
    combines CSV files from different stations into a single file, and compresses and archives the original CSV files, stripping out corrupted lines
    Runs a SAS statistical program that performs range checks and merges with previous data
    Runs another SAS job that updates graphics and reports for the current month

## Slide 27: Workflow output

## Slide 28: A “Manual” Workflow
The previous example spanned a variety of:
  Computer operating systems
    Windows /MSDOS
    Unix/Linux
  Software
    Proprietary software (Loggernet)
    MSDOS Batch file, Windows Scheduler
    Unix/Linux Shell / Crontab scheduler
    SAS
It required that configurations be set up on several systems, and a significant amount of documentation
Is there a better way?

## Slide 29: Scientific Workflow Systems
Scientific Workflow Systems such as Kepler, Taverna, Vis-trails and others integrate diverse tools into a single coherent system, with a graphical interface to help keep things organized
Individual steps in a process are represented by boxes on the screen that intercommunicate to produce a complete workflow
Kepler has good support for the “R” statistical programming language

## Slide 30
Sample Kepler Workflow for QA/QC